## Slide 1: SE511 Strategic Military Sensors Projects assignments
Dr Ir Xavier Neyt
Professor
Royal Military Academy
Brussels, Belgium

## Slide 2: Content
Optical images
  Hyperspectral Unmixing
  Registration
  Co-registration
  Orthorectification
  Sentinel-2 image: classification
Radar images
  SAR image: effect of cloud / rain
  SAR image: temporal de-speckling
Generally speaking:
  Dataset available on BelADL

## Slide 3: Initial conditions
Projects are to be conducted individually
A report is expected, presenting
  What was done
    Describe the methodology
  The results
    Including intermediate results
  A meaningful & critical analysis
    How did you verify that your results were correct?
    Are your results plausible/reasonable?

## Slide 4: Hyperspectral unmixing
Dataset:
  http://www.ehu.eus/ccwintco/index.php/Hyperspectral_Remote_Sensing_Scenes
ToDo:
  Extract endmembers from the scene
  Evaluate abundance
  Ground truth is available
Color corresponds
to a class
(concrete, grass, …)

## Slide 5: Co-Registration
Image 1 - image 2
ToDo:
  Extract GCP (1 a 2)
  Compute transform (using a subset of the GCP)
  Compute residuals (on unused GCP)
  Resample the image

## Slide 6: Registration
Image 1 - Google Earth
ToDo:
  Similar to Co-registration
  Produce KML file…

## Slide 7: Orthorectification
Image 1 + Digital Elevation Model
  + Imaging geometry (focal length)
ToDo:
  Indirect method suggested
  Retrieve altitude from DEM
  Compute pixel location in image
  Interpolate

## Slide 8: Sentinel2-classification
Sentinel-2 image
ToDo:
  Compute band ratios NDVI, NDBI and NDWI
  Classify image according to results

## Slide 9: Sentinel1-Effect of clouds
Sentinel-1 image
Central questions: is there a link between clouds & backscatter
  Extract cloud map (S2)
  Compute sigma0 statistics (mean) when there are clouds & when there are no clouds
    Remove effect of sigma0 fluctuations
  Analyse results

## Slide 10: Sentinel1-Despeckling
Sentinel-1 image
Despeckling
  Spatially: Lee-filter : variance/mean over neighbouring pixels
  Temporal Lee-filter: variance/mean over time-neighbouring pixels
    Exploit S1 time series

## Slide 11: Final recommendations
Start working now!
  Do not procastinate…
Report due Dec 7th
Should you be stuck or have question
Come and find us!
  Make an appointment beforehand…